## Slide 1: Construction
Task A: Using formulae in the construction industry
1) Here are the front and side elevations of a shed.
A builder needs to replace the rafters of the shed.
How long are the rafters?
2.8 m
3 m
4 m
2.5 m
Water runs through a cylindrical pipe at a velocity of 10 m/s.
The diameter of the pipe is 40 mm.
What is the flow rate in m3 per hour?
2) Q = A × v
where Q is the flow rate, A is the flow area and v is the velocity

## Slide 2
Construction
4) BTU = volume of the room × allowance for heat loss
Below are the dimensions of a bedroom.
Length = 4.6 m
Width = 2.6 m
Height = 2.4 m
a) Calculate the BTU.
b) The bedroom will have one radiator.
Which size should be installed?
Room | Allowance
Bathroom | 121.5
Bedroom | 108
Dining room | 135
Hallway | 81
Kitchen | 81
Living room | 135
Height (mm) | Width (mm) | BTU
600 | 400 | 2184
600 | 600 | 3280
600 | 800 | 4372
600 | 1000 | 5464
600 | 1200 | 6556
600 | 1400 | 7649
600 | 1600 | 8744
The voltage of electricity in UK households is 230 volts.
An electrician needs to install a 2.15 kW electric oven.
Circuits are available in 6, 10, 16, 20, 32, 40, 50 and 63 amps.
Which circuit should be installed?
3) P = I × V
where P is the power (watts) , I is the current (amps) and V is the voltage (volts)

## Slide 3
Construction
Mathematics in Education and Industry
v2.4
Task B: Costing in the construction industry
1) This table shows the prices and lengths wood is sold in.
Calculate the cheapest price for purchasing the following:
a) Twenty 1 m lengths
b) Fifteen 1.8 m lengths
c) 3 different ways to buy 600 1.2 m lengths
d) Why are there 3 different ways for part (c)?
Length (mm) | Price
2400 | £4.20
3000 | £5.25
3600 | £6.30
4200 | £7.35
4800 | £8.40